## Slide 1: Dual Camera Calibration

## Slide 2: 校正环境与规格
测试环境
  光源： 可见光 : 2900 ± 100 Lux, 6500K± 200K UV光 365nm : TBD (成像亮度均匀且对比度高)
  测试距离：120mm/200mm
  Chart：漫反射标定板
  Chart Pattern : 12x9 棋盘格
  Chart : 购买参考连结, GP150与GP200
校正规格
  X Shift < TBD
  Y Shift < TBD
  Rotation < +/- 1.5˚
DUT
120mm/ 200mm
可見光
可見光
UV光
UV光

## Slide 3: Dual Camera Calibration DLL
namespace NST {
  public ref struct Image { // calibration 輸入的資料格式
    array<System::Byte>^ data;
    int width;
    int height;
    int channels;
  };
  public enum class ErrCode { // calibration回傳的error code
    Pass = 0,
    Fail = 1
  };
  public ref class DualCameraCalibration { // 主要類別
    public:
    DualCameraCalibration() {};
    ~DualCameraCalibration() {};
    ref struct CaliResult {{ // calibration回傳的校正結果,請依SN記錄到產測log (ex:csv檔)
      int dx;
      int dy;
      double rotate;
    };
    System::ValueTuple<ErrCode, CaliResult^> calibration(Image^ rgb, Image^ uv); // 雙目校正API,輸入rgb與uv影像
  };
}
具體引用方式可參考demo code: dual_camera_calibration.7z

## Slide 4: EEPROM Contents
名稱 | 位址 | Size(Byte) | Contents
Header | 0x00 | 2 | 0x55AA
Board Name | 0x02 | 11 | ‘K’,’U’,’N’,’L’,’U’,’N’,’-’,D’,’U‘,’A’,’L’
HW Version | 0x0D | 2 | TBD
Serial Number | 0x0F | 16 | TBD
Reserved | 0x20 | 15 | Reserved
Near Distance | 0x30 | 1 | Near calibration distance in cm, 0x00 means no calibration
Far Distance | 0x31 | 1 | Far calibration distance in cm, 0x00 means no calibration
Reserved | 0x32 | 13 | Reserved
Near X shift | 0x40 | 2 | Near Distance X shift
Near Y shift | 0x42 | 2 | Near Distance Y shift
Near Rotation | 0x44 | 1 | Near Distance Rotation (CaliResult.rotate * 10)
Far X shift | 0x45 | 2 | Far Distance Far X shift
Far Y shift | 0x47 | 2 | Far Distance Far Y shift
Far Rotation | 0x49 | 1 | Far Distance Far Rotation (CaliResult.rotate * 10)
Reserved | 0x4A | TBD | Reserved
HW info (TBD)
Calibration info
Calibration results

## Slide 5
Q&A